## Slide 1: Test on New VA1140
11/Mar/2022
G. Ambrosi, M. Barbanera, M. Caprai, M. D'Antonio, M. Duranti, M. Ionica, G. Silvestre

## Slide 2
1. Glue 2 "VA1140" on FOOT PCB Hybrid
 everything is fine

## Slide 3
2. Glue the other 8 "VA1140"
Calibration with 10 VA (but no silicon)

## Slide 4
3. Gluing a FOOT silicon sensor
Thickness | 150um
Overall dim | 102.5mmx103.5mm
Active area | 96mm x 96mm
Strip pitch | 50 um
Readout pitch in Foot | 150 um
Number of readout strips | 640
Dispensing the conductive glue (Epotek EJ2189) and siliconic glue (DC 3145 grey) for the silicon sensor gluing on PCB
Positioning the silicon sensor on the PCB
Performing wire bonding
Calibration with sensors

## Slide 5
FOOT-newVA: pedestals
FOOT-newVA: sigma
FOOT-newVA: sigma raw
channel
channel
channel
Thickness | 150um
Overall dim | 102.5mmx103.5mm
Active area | 96mm x 96mm
Strip pitch | 50 um
Readout pitch in Foot | 150 um
Number of readout strips | 640
FOOT sensor:
+ new batch of VAs

## Slide 6
channel
channel
channel
AMS-flight ladder:
- Layer2
- "slot" 9

## Slide 7
FOOT-newVA: pedestals
FOOT-newVA: sigma
FOOT-newVA: sigma raw
channel
channel
channel
channel
channel
channel

## Slide 8
3. Test with laser

## Slide 9
3. Test with laser

## Slide 10
3. Scan in "trigget to hold"

## Slide 11
4. Power consumption
Current: measured (datasheet) @ voltage  power consumption
VDD: 1.67 mA (1.3 mA) @ 1.5V  2.505 mW
VSS: 6.37 mA (9.5 mA) @ -2.0V  12.74 mW
Total consumption per chip: 15.245 mW
Consumption per channel: ~ 0.25 mW
Total consumption per ladder ~ 0.26 W
Total consumption per L0 (72 ladders) ~ 18 W